## Slide 1: Flight Testing Small UAVs for Aerodynamic Parameter Estimation
Adam T. Chase and Robert A. McDonald
California Polytechnic State University

## Slide 2: Motivation
Lack of small uav lift/drag regression models

## Slide 3: Goals
Integrate air data acquisition system into flight vehicle
Measure drag polar and lift curve slope from flight test
Quantify changes in vehicle performance from configuration changes

## Slide 4: Equations of Motion
Newton’s 2nd Law, in body axes:
Fixed mass assumption (electric aircraft):
Applied forces:
Assume no thrust:

## Slide 5: Assumptions
Re-arrange terms:
Rotate from body to wind axes:
where
Only an accelerometer and an air data system are required to get lift/drag forces in gliding flight

## Slide 6: Sensor Selection
Analog Devices ADXL-362
  +/- 8G range
  SPI interface
  Ultra-low noise (175 μG/)
  Available as SMD and breakout board
Air Data System
  Five-hole probe from Aeroprobe
    6” x 1/8” OD tube
    Calibrated angles to pressures at 70 ft/s
  All Sensors’ 5-INCH-D-DO differential pressure transducer
    +/- 5” H20 range
    Digital serial interface
    0.5% FSO noise

## Slide 7: Additional Sensors
ITG-3200 gyroscope
  Euler angles
U-Blox LEA-6T GPS receiver
  Euler angle correction, flight visualization
HMR-2300 magnetometer
  High accuracy, used for slow or vertical flight
HMC-5883L magnetometer
  Small, inexpensive
Barometric pressure transducer
  Barometric pressure/altitude
DS18B20 temperature sensor
  Allows density/air speed calculation
Servo PWM signal
  Isolates flight without throttle

## Slide 8: Simulator Development
Modified de Havilland Beaver 6-DOF simulator from Simulink
  Scaled mass and moments of inertia to R/C aircraft
  Replaced aero forces with drag polar
  Removed engine forces and moments
  Output required state to workspace for comparison to estimate
Notes: Simulator modifications

## Slide 9: Simulation Output
Verified drag polar estimation method
Helped develop data analysis routines
Aided flight test planning
Notes: Hey look, simulator is working

## Slide 10: Random Error
Notes: Now we use sim to propagate random error, and we note heteroskedasticity

## Slide 11: Regression Error
Error of regression driven by confidence intervals
  If the experiment is repeated, the regression coefficients will lie in this interval n% of the time
Error in data is heteroskedastic for random error
  not affected by heteroskedasticity
  Confidence intervals affected by heteroskedasticity
  Matlab’s “robustfit” function returns robust standard error estimates
Can also use Kalman filter to estimate coefficients
  Zero process noise, no state update
t = 1.96 for 95% CI
Notes: With random error propagated, we try to fit curve and deal with heteroskedasticity

## Slide 12: Heteroskedasticity
Insert table of error values here
Notes: Hey look how awesome robust regression is.

## Slide 13: System Architecture

## Slide 14: Calibration – Accel/Gyro
Data collected with a known magnitude
  1G for accelerometer, 33 1/3 RPM for gyro (turntable)
Nonlinear least squares:
  where

## Slide 15: Calibration - Magnetometers
Soft- and Hard-iron effects removed with least squares
  Centers ellipse around zero
  Scales each axis to turn ellipse into a sphere
Alignment through rotation matrix

## Slide 16: Air Data System Integration

## Slide 17: Calibration – Air Data System
Alignment calibration:
  Known alignment between adapter and probe
  Calibrate accelerometer on adapter
  Measure rotation between probe accelerometer and body accelerometer
Zero-offset removed pre-flight
Slope calibrated with nVision’s Reference Pressure Recorder
Angles calibrated to pressures from the manufacturer

## Slide 18: Calibration – Environmental

## Slide 19: Flight Test

## Slide 20: Future Work