## Slide 1: Flight Testing Small UAVs for Aerodynamic Parameter Estimation
Adam Chase

## Slide 2: Motivation
Wind tunnel access limited
  Full-scale testing often unavailable
Smaller vehicles generally not in steady-level flight
Provide intelligent design decisions based on test flight
Many potential uses for accurate sensing of small UAVs

## Slide 3: Thesis Goal
Top level: determine full-scale performance of small R/C aircraft
  Drag polar, CL – α curve, etc.
Secondary goal: ensure apparatus can be expanded for other flight test uses
  Stability derivatives
  Dynamic thrust measurements

## Slide 4: Previous Work
Assume dynamics model is known
  Wind Field Estimation for Small Unmanned Aerial Vehicles, Langelaan et al. 2010
Assume no wind, or no vertical wind
  Angle of Attack and Sideslip Estimation Using an Inertial Reference Platform, Zeis. 1988
Used autopilot to stabilize vehicle
  Flight Testing Small, Electric Powered Unmanned Aerial Vehicles, Ostler. 2006
Assume linearization about maneuver
  Real-Time Aerodynamic Parameter Estimation Without Air Flow Angle Measurements, Klein and Morelli. 2012
Notes: These aren’t exclusive. For instance. No wind/no vertical wind needs this assumption OR a dynamics model

## Slide 5: Equations of Motion
acts in wind axes > requires α, β
acts in inertial axes > requires
measured in body axes

## Slide 6: Assumptions
No Coriolis effect
Fixed mass system
Folding propeller used and turned off for test
+ )
+ )
)
+ )

## Slide 7: Required Sensors
Minimum required state:
Corresponding sensors:
  5-hole probe
  3 differential pressure sensors
  3-axis compass/magnetometer
  3-axis accelerometer
  Postal scale

## Slide 8: Error Propagation for a Given Point
Notes: Update plot to current sensors and remove fits

## Slide 9: Data Fitting
Error of regression driven by confidence intervals
  If the experiment is repeated, the regression coefficients will lie in this interval n% of the time
Error in data is heteroskedastic
  not affected by heteroskedasticity
  Confidence intervals affected by heteroskedasticity
  Matlab’s “robustfit” function returns robust standard error estimates
Can also use Kalman filter to estimate coefficients
  Zero process noise, no state update
Z = 1.96 for 95% CI

## Slide 10: Improving Point Error
Cascaded Kalman filters to improve single-point error
  Discrete Kalman filter for Euler angles
    Adds to required states
  Extended discrete Kalman filter for wind angles

## Slide 11: New Required Sensors
Required state with filters:
Corresponding sensors:
  5-hole probe
  3 differential pressure sensors
  3-axis compass/magnetometer
  3-axis accelerometer
  Postal scale
  3-axis gyroscope

## Slide 12: Simulation
Built-in DHC-2 Beaver 6DOF Simulink model
Based on curve fits to flight test data
Non-linear forces and moments
Partially connected to Flight Gear

## Slide 13: Simulator Modifications
Scaled mass and moments of inertia to R/C aircraft
Replaced aero forces with drag polar
Removed engine forces and moments
Improved Flight Gear visualization
Output required state to workspace for comparison to estimate

## Slide 14: Result: No Added Noise
Verified equations of motion match the simulated dynamics

## Slide 15: Model Fit with Noise

## Slide 16: Accuracy of Model
Actual coefficients [K2 K1 CD0]:
0.0493 0.0000 0.0300
Estimated coefficients :
0.0512 -0.0055 0.0316
Estimated coefficients using 'robustfit' function:
0.0488 -0.0023 0.0310
95.0% CI from 'regress' function :
0.0522/0.0503 -0.0045/-0.0065 0.0320/0.0313
95% CI from 'robustfit' function :
0.0497/0.0480 -0.0014/-0.0032 0.0313/0.0307
Percent error in estimated coefficients:
3.7120 0.5498 5.2035
Percent error in estimated coefficients from 'robustfit':
-1.0104 0.2338 3.1762

## Slide 17: Sensor Selection
Honeywell HMR2300 Magnetometer
  0.2o pitch, 0.1o roll
  5V board
  UART interface
Invense ITG-3200 rate gyro
  0.38 o/s - rms
  3.3V board
  I2C interface
Size:
1.96 x 1.65 x 0.52 inches
Size: 0.7 x 0.55 inches

## Slide 18: Sensor Selection (cont’d)
Analog Devices ADXL362
  1 mg/LSB, 175μg/
  3.3V board
  SPI interface
3x All Sensors 5 INCH-D-DO Diff. Press.
  0.25% FS
  5V
  SPI
Size: 0.55x 0.6 inches
Size: 1.08 x 1.0 x 1.1 inches

## Slide 19: Sensor Selection (cont’d)
adaFruit microSD Card Shield
  FAT32 capable
    Max 4GB file size
  3.3V board
  SPI interface
Logic Level Converter
  Converts 5V sensors to 3.3V
  2 bi-directional channels
Size:
1.25 x 1.0 x 0.15 inches
Size: 0.5 x 0.6 inches

## Slide 20: Sensor Selection (cont’d)
Aeroprobe 5 Hole Air Data probe
  <1o from mfg
  0.2o from A&M
  1/8” OD
  0.3o expected
  Max angle = 45o

## Slide 21: Additional Sensors
uBLOX LEA-6T GPS Receiver
  Raw data available
  3.3V board
  UART,USB,I2C
All Sensors BARO-INHG-DO Abs. Press.
  10 mBar
  5V board
  SPI
Size: 1.08 x 1.0 x 1.1 inches

## Slide 22: Flight Computer
Arduino Due
  32 bit 84 MHz ARM processer
  512 Kbytes Flash RAM
  54 digital I/O, 12 analog-in (12 bit)
  3.3 V I/O pins
  4 UART ports
  USB Host
  7-20V power

## Slide 23: Flight Test Vehicles
0.60 size Telemaster
Motor Glider
Small flying wing

## Slide 24: Completed Work (1/2)
Method developed
Simulated results with nonlinear plant
Added noise and derived sensing requirements
Arduino taking data from most sensors to SD card
Data from SD card plotted in MATLAB

## Slide 25: Completed Work (2/2)
Purchased all hardware
Found multitude of hardware integration issues
Stationary noise estimate from gyro and accelerometer
Reading magnetometer and GPS with RS232
Eagle PCB files in process

## Slide 26: Sensor Calibration
Expected tasks:
  -Gyro/accel calibration using rotary movement
  -Magnetometer calibration routine built in
  - α,β come factory calibrated

## Slide 27: Aircraft Integration
Expected tasks:
  Re-calibrate sensors once in vehicle
  EMI for GPS/Motor/ESC/Compass
  Air data integration
  Make necessary changes for validation

## Slide 28: Flight Testing
Expected tasks:
  Flight test planning and documentation
  Fairly gentle flight (no loops/rolls)
  Add sensing of throttle input to mark beginning of test
    Possibly couple with data logging to not overflow file size limit

## Slide 29: Validation Methods
CD0: add parachutes
  ΔCD0 from 0 → 1 chutes = ΔCD0 from 1 → 2 chutes
K1: change wing camber
  Changes CLmin and shifts polar vertically
K2: change wing aspect ratio
  Prandtl 3-d correction (Anderson pg. 444)

## Slide 30: Final Product
Integrate custom data acquisition system into flight vehicle
Measure drag polar and lift curve slope from flight test
Quantify changes in vehicle performance from configuration changes
Notes: Things we haven’t been able to do in the past