## Slide 1: Flight Testing Small UAVs for Aerodynamic Parameter Estimation
Adam T. Chase and Robert A. McDonald
California Polytechnic State University

## Slide 2: Motivation
Lack of small UAV lift/drag regression models
Small UAVs do not fly “steady-level”
Designers need data to conduct quantitative trades
Off the shelf systems not sufficient
  No air data system
  Closed source, lack of error propagation

## Slide 3: Goals
Integrate air data acquisition system into flight vehicle
Measure drag polar and lift curve slope from flight test
Quantify changes in vehicle performance from configuration changes

## Slide 4: Equations of Motion
Newton’s 2nd Law, in body axes:
Fixed mass assumption (electric aircraft):
Applied forces:
Assume no thrust:

## Slide 5: Assumptions
Re-arrange terms:
Rotate from body to wind axes:
where
Only an accelerometer and an air data system are required to get lift/drag forces in gliding flight

## Slide 6: Sensor Selection
Analog Devices ADXL-362
  +/- 8G range
  SPI interface
  Ultra-low noise (175 μG/)
  Available as SMD and breakout board
Air Data System
  Five-hole probe from Aeroprobe
    6” x 1/8” OD tube
    Calibrated angles to pressures at 70 ft/s
  All Sensors’ 5-INCH-D-DO differential pressure transducer
    +/- 5” H20 range
    Digital serial interface
    0.5% FSO noise

## Slide 7: Additional Sensors
ITG-3200 gyroscope
  Euler angles
U-Blox LEA-6T GPS receiver
  Euler angle correction, flight visualization
HMR-2300 magnetometer
  High accuracy, used for slow or vertical flight
HMC-5883L magnetometer
  Small, inexpensive
Barometric pressure transducer
  Barometric pressure/altitude
DS18B20 temperature sensor
  Allows density/air speed calculation
Servo PWM signal
  Isolates flight without throttle

## Slide 8: Simulator Development
Modified de Havilland Beaver 6-DOF simulator from Simulink
  Scaled mass and moments of inertia to R/C aircraft
  Replaced aero forces with drag polar
  Removed engine forces and moments
  Output required state to workspace for comparison to estimate
Notes: Simulator modifications

## Slide 9: Simulation Output – No Noise
Verified drag polar estimation method
Helped develop data analysis routines
Aided flight test planning
Notes: Hey look, simulator is working

## Slide 10: Random Error
Notes: Now we use sim to propagate random error, and we note heteroskedasticity

## Slide 11: Regression Error
Error of regression driven by confidence intervals
  If the experiment is repeated, the regression coefficients will lie in this interval n% of the time
Error in forces for random error is heteroskedastic
Matlab’s robustfit returns robust standard error estimates
  De-weights heteroskedastic outliers using iteratively weighted least squares
t = 1.96 for 95% CI
Notes: With random error propagated, we try to fit curve and deal with heteroskedasticity

## Slide 12: Heteroskedasticity
 | CD0 | K1 | K2
System Inputs | 0.0493 | 0 | 0.03
OLS Estimate | 0.0355 | -0.0136 | 0.0275
Robust LS Estimate | 0.0460 | -0.0037 | 0.0292
Notes: Hey look how awesome robust regression is.

## Slide 13: System Architecture
Aeroprobe Five-Hole Probe
Calibrated angles to pressures at 70 ft/s
External Air Data System
Custom PCB
Pressure, temperature, and alignment accel
RJ-25 interface
Data Acquisition Shield
Custom PCB
Integrates external mag, pressure sensors
Customizable to fit packaging needs
Arduino Due Flight Computer
84 MHz clock
32-bit processor
4 UART channels
+

## Slide 14: Calibration – Accel/Gyro
Data collected with a known magnitude
  1G for accelerometer, 33 1/3 RPM for gyro (turntable)
Nonlinear least squares:
  where

## Slide 15: Calibration - Magnetometers
Soft- and Hard-iron effects removed with least squares
  Centers ellipse around zero
  Scales each axis to turn ellipse into a sphere
Alignment through rotation matrix

## Slide 16: Calibration – Air Data System
Alignment calibration:
  Known alignment between adapter and probe
  Calibrate accelerometer on adapter
  Measure rotation between probe accelerometer and body accelerometer
Zero-offset removed pre-flight
Slope calibrated with nVision’s Reference Pressure Recorder
Angles calibrated to pressures from the manufacturer

## Slide 17: Air Data System Integration

## Slide 18: Flight Test

## Slide 19: Flight Crash

## Slide 20: Future Work
Verify system accuracy
Integrate sensors into an INS solution
Instrument for in-flight thrust measurement
Stability/control derivative estimation